RESOLUTION #2020-009

A RESOLUTION OF THE LAKE FOREST ESTATES CLEAN WATER DISTRICT ESTABLISHING RULES AND REGULATIONS FOR THE OPERATION OF THE WASTEWATER SYSTEM OF THE LAKE FOREST ESTATES SUBDIVISION LOCATED IN STE. GENEVIEVE COUNTY, MISSOURI.

WHEREAS, the owners of the Lake Forest Estates Subdivision (the “Subdivision”) in Ste. Genevieve County, Missouri incorporated the Lake Forest Estates Clean Water District (the “District”) as a Reorganized Common Sewer and Water District pursuant to Section 204.602 et seq. of the Revised Statutes of Missouri and by order of the Ste. Genevieve County Circuit Court effective on November 12, 2019; and

WHEREAS, the District was incorporated to acquire, operate, and maintain the Subdivision’s existing water distribution and wastewater facilities (the “Systems”), which duties included the financing and construction of certain improvements to the wastewater facilities to bring same into compliance with federal and state clean water regulations; and

WHEREAS, the owners of the Subdivision have approved the transfer of the Systems to the District, and the Subdivision has entered into a contract with the District for such transfer, effective not later than December 31, 2020, after which the District shall own, control, and operate the Systems; and

WHEREAS, the District has applied for financing to construct improvements to the Wastewater System and has further taken steps to assume ownership, control, and operation of the Systems as of December 31, 2020, or such earlier time as circumstances allow; and

WHEREAS, pursuant to its authority under Section 204.602 et seq. RSMo. and to establish the parameters by which the District shall operate the Wastewater System, the Board of Trustees of the District desires to enact these rules and regulations;

NOW, THEREFORE, BE IT RESOLVED BY THE LAKE FOREST CLEAN WATER DISTRICT OF STE. GENEVIEVE COUNTY, MISSOURI, AS FOLLOWS:

Section 1.  The following Rules and Regulations for the Wastewater System serving the Lake Forest Estates Clean Water District are hereby enacted:

Article I:  Scope and Authority.

A.	A.	These Rules and Regulations apply to: (i) all owners of property located within the Lake Forest Estates Clean Water District as of the effective date of the District’s acquisition and operation of the water supply and wastewater facilities of the Lake Forest Estates Subdivision, Ste. Genevieve County, Missouri (existing wastewater users) and (ii) all future District wastewater users.

B.	These Rules and Regulations have been adopted to govern the wastewater services furnished by the District in a uniform manner and for the benefit of the District and its water users.  The Rules and Regulations may be amended at any regular meeting of the District, or at any special meeting thereof called for such purpose. Except as provided in Section 1.C hereof, they are subject to amendment without notice to any water user or any other person.

C.	These Rules and Regulations, and any amendments thereto have been and remain subject to the approval of the State Director of the United States Department of Agriculture, Rural Development, for so long as the District has unpaid obligations which are held or insured by the United States of America. The State Director shall be timely notified of any amendment, and such amendment shall be effective on the date of its enactment by the District or on such other date as the District may designate in its amending resolution. Such amendment shall be ineffective only if not approved by the USDA, Rural Development, but in the event such approval is given by the USDA, Rural Development, said approval shall be retroactive to the date of such amendment.

D.	If any portion of these Rules and Regulations shall be declared invalid by competent authority, such invalidity shall not affect the validity of the remaining portion.

Article II: Definitions.

The following words and terms shall have the following meanings:

Applicant:  Any individual, firm, partnership, corporation, the Federal or State Government, or any unit, agency, political corporation or subdivision of either the Federal or State Government, or other agency applying for wastewater service.

Board:  The Board of Trustees of the Lake Forest Estates Clean Water District, Ste. Genevieve County, Missouri.

BOD (Biochemical Oxygen-Demand): The quantity of oxygen utilized in the biochemical oxidation of organic matter under standard laboratory procedure in five (5) days at 20o C, expressed in milligrams per liter.

Building Drain: That part of the lowest horizontal piping of a drainage system which receives the discharge from soil, waste, and other drainage pipes inside the walls of a building and conveys it to the building sewer, beginning five (5) feet (1.5 meters) outside the inner face of the building wall.

Building Sewer: The extension from the building drain to the public sewer or other place of disposal.

Combined Sewer:  A sewer receiving both surface runoff and sewage.

District: The Lake Forest Estates Clean Water District, Ste. Genevieve County, Missouri.

Garbage: Solid wastes from the domestic and commercial preparation, cooking, and dispensing of food, and from the handling, storage and sale of produce.

Industrial Wastes: The liquid wastes from industrial manufacturing processes, trade or business as distinct from sanitary sewage.

Inspector: The person or persons duly authorized by the District to inspect and approve the installation of building sewers and their connection to the public sewer system.

Natural Outlet: Any outlet into a watercourse, pond, ditch, lake or other body of surface or groundwater.

Person: Any individual, firm, company, association, society, corporation or group.

pH:  The logarithm of the reciprocal of the weight of hydrogen ions in grams per liter of solution.

Properly Shredded Garbage: The wastes from the preparation, cooking and dispensing of foods that have been shredded to such a degree that all particles will be carried freely under the flow conditions normally prevailing in public sewers, with no particle greater than one-half (1/2) inch (1.27 centimeters) in any dimension.

Public Sewer: A sewer in which all owners of abutting properties have equal rights and is controlled by the District.

Sanitary Sewer: A sewer which carries sewage and to which storm, surface and ground waters are not intentionally admitted.

Sewage: A combination of the water-carried wastes from residences, business buildings, institutions, and industrial establishments, together with such ground, surface and storm waters as may be present.

Sewage Treatment Plant: Any arrangement of devices and structures used for treating sewage.

Sewage Works: All facilities for collecting, pumping, treating and disposing of sewage.

Sewer: A pipe or conduit for carrying sewage.

Slug: Any discharge of water, sewage or industrial waste which in concentration of any give constituent or in quantity of flow exceeds for any period of duration longer than fifteen (15) minutes more than five (5) times the average twenty-four (24) hour concentration or flows during normal operation.

State Director: The State Director of Rural Development for Missouri, United States Department of Agriculture, or his successor.

Storm Drain (or Storm Sewer): A sewer which carries storm and surface waters and drainage, but excludes sewage and industrial wastes, other than unpolluted cooling water.

Superintendent: The wastewater superintendent of the District.

Suspended Solids: Solids that either float on the surface of, or are in suspension in water, sewage, or other liquids and which are removable by laboratory filtering.

Watercourse: A channel in which a flow of water occurs, either continuously or intermittently.

Article III:  Public Sewer Connections.

A.	Connection Required, When.

1.	Except as provided in Article IV hereof, the owner of all houses, buildings or properties used for human occupancy, employment, recreation or other purposes, situated within the District and abutting on any street, alley or right-of-way in which there is now located or may be in the future be located a public sanitary or a combined sewer of the District is hereby required at his or her expense to install suitable toilet facilities and building drains therein and to connect such facilities directly with the proper public sewer within ninety (90) days after date of official notice to do so, provided that said public sewer is within one hundred (100) feet (30.5 meters) of the property line.

2.	A separate and independent building sewer shall be provided for every building, except where one building stands at the rear or on an interior lot and no private sewer is available or can be constructed to the other building through an adjoining alley, court, yard or driveway. In such case the building sewer from the front building may be extended to the other building and the whole considered as one building sewer, upon approval by the District.

3.	Existing building sewers may be maintained for existing buildings, but any repair or replacement of existing building sewers shall be permitted in accord with Paragraph C of this Article. Existing building sewers may be used in connection with new buildings if they are found, on examination and test by the Inspector, to meet all requirements of this resolution.

B.	Permit Required.

1.	No unauthorized person shall uncover, make any connections with or opening into, use, alter, or disturb any public sewer or appurtenance thereof without first obtaining a written permit from the Inspector.

2.	There shall be two classes of building sewer permits: (a) for residential and commercial service and (b) for service to establishments producing industrial wastes.  In either case, the owner shall make application in a form provided by the District, and the application shall be accompanied by a permit and inspection fee determined by the District from time to time and included in the District’s rate schedule. The application shall include such plans, specifications, or other information considered pertinent in the judgment of the Inspector.

C.	Construction.

1.	All costs and expense incident to the installation and connection of the building sewer shall be borne by the owner.  The owner shall indemnify the District from any loss or damage that may directly or indirectly be occasioned by the installation of the building sewer.

2.	The size, slope, alignment, materials, and methods to be used in constructing and connecting a building sewer to the public sewer, and the excavating, placing of the pipe, jointing, testing and back filling of the trench, shall: (a) conform to the requirements of any building code, plumbing code, or other applicable rules and regulations adopted by the District, or (b) in the absence of same, shall utilize industry appropriate materials and be constructed in a good and workmanship like manner as is reasonably determined by the Inspector and in a manner consistent with any applicable guidance from the Missouri Department of Natural Resources. All connections shall be made gas-tight and water-tight.

3.	Whenever possible, the building sewer shall be brought to the building at an elevation below the basement floor.  In all buildings in which any building drain is too low to permit gravity flow to the public sewer, sanitary sewage carried by such building drain shall be lifted by an approved means and discharged to the building sewer.

4.	The applicant for the building sewer permit shall notify the Inspector when the building sewer is ready for inspection and connection to the public sewer.  The connection shall be made under the supervision of the Inspector or his representative.

5.	All excavations for building sewer installations shall be adequately guarded with barricades and lights so as to protect the public from hazard, streets, sidewalks, parkways and other public property disturbed in the course of the work shall be restored in a manner satisfactory to the District.

Article IV:  Inspector’s Authority.

A.	The Inspector is hereby authorized to inspect, observe, sample, measure, and test: (1) any work at any stage of construction, (2) any building drain or building sewer suspected of leakage, damage, or being in need of repair or maintenance, (3) any equipment related to a suspected violation of this resolution or other law, rule, or regulation, or (4) for any other reason permitted by this resolution or other law, rule, or regulation.

B.	An owner or applicant shall notify the Inspector when the work is ready for final inspection and before any underground portions are covered.

C.	The Inspector shall bear proper credentials and identification, and on presentation thereof to the owner shall be permitted to enter all properties for the purposes provided herein as a condition of the District providing wastewater service.

D.	The Inspector shall have no authority to inquire into any processes, including metallurgical, chemical, oil, refining, ceramic, paper, or other industries, beyond that point having a direct bearing on the kind and source of discharge to the sewers or waterways or facilities for waste treatment.

E.	All entry, inspection, and subsequent work, if any, by the Inspector or the District on private property shall be done in full accordance with the terms of any District easement pertaining to private property, and the District shall be required to repair any damage caused to the property by the District’s entry, inspection, and work.

Article V: Unlawful and Regulated Discharges.

A.	Unlawful Discharges. No person shall discharge or cause to be discharged any of the following described waters or wastes to any public sewer:

- Storm water, surface water, ground water, roof runoff, subsurface drainage, including interior and exterior foundation drains, uncontaminated cooling water or unpolluted industrial process waters;

- Any gasoline, benzene, naphtha, fuel oil or other flammable or explosive liquid, solid, or gas;

- Any waters or wastes containing toxic or poisonous solids, liquids or gases in sufficient quantity, either singly or by interaction with other wastes, to injure or interfere with any sewage treatment process, constitute a hazard to humans or animals, create a public nuisance, or create any hazard in the receiving waters of the sewage treatment plant, including but not limited to cyanides in excess of two (2) mg/1 as CN in the wastes as discharged;

4.	Solid or viscous substances in quantities or of such size capable of causing obstruction or other interference with the proper flow and operation of the sewage works such as, but not limited to, ashes, cinders, sand, mud, straw, shavings, metal, glass, rags, feathers, tar, plastics, wood, unground garbage, whole blood, paunch manure, hair and fleshings, entrails and paper dishes, cups, milk containers, etc., either whole or ground by garbage grinders; or

5.	Any wastes regulated by Article VI, Section B hereof in violation of the requirements of said section or the determinations of the Inspector or Superintendent as provided therein.

B.	Regulated Discharges. The following may be discharged to a public sewer only on compliance with the regulations provided herein or the determinations of the Inspector or the Superintendent as provided herein.

- Any waters or wastes (a) having a five-day biochemical oxygen demand greater than 300 parts per million by weight, (b) containing more than 350 parts per million by weight of suspended solids, or (c) having an average daily flow greater than two percent of the average sewage flow of the District, shall be subject to the review and determination of the Superintendent. When necessary, in the opinion of the Superintendent, the owner shall provide, at his expense, such preliminary treatment as may be necessary to (i) reduce the biochemical oxygen demand to 300 parts per million by weight or (ii) reduce the suspended solids to 350 parts per million by weight or (iii) control the quantities and rates of discharge of such waters or wastes.  Plans, specifications and any other pertinent information relating to proposed preliminary treatment facilities shall be submitted for the approval of the Superintendent, and no construction of such facilities shall be commenced until said approvals are obtained in writing and until a permit has been applied for to the District and issued by the Inspector.

2.	Any substances, materials, waters, or wastes if it appears likely in the opinion of the Inspector that such wastes can (a) harm either the sewers, sewage treatment process or equipment, (b) have an adverse effect on the receiving stream, or (c) can otherwise endanger life, limb, public property, or constitute a nuisance.  In forming his opinion as to the acceptability of these wastes, the Inspector will give consideration to such factors as the quantities of subject wastes in relation to flows and velocities in the sewers, the materials of construction of the sewers, the nature of the sewage treatment process, the capacity of the sewage treatment plant, the degree of treatability of wastes in the sewage treatment plant, and any other pertinent factor. The substances so regulated are:

- Any liquid or vapor having a temperature higher than one hundred fifty (150)o F (65oC);

- Any water or waste containing fats, wax, grease or oils, whether emulsified or not, in excess of one hundred (100) mg/1 or containing substances which may solidify or become viscous at temperatures between thirty two (32) and one hundred fifty (150)o F (0 and 65o C);

- Any garbage that has not been properly shredded (the installation and operation of any garbage grinder equipped with a motor of three-fourths (3/4) horsepower (0.76 hp metric) or greater shall be subject to the review and approval of the Inspector);

- Any waters or wastes containing strong acid iron pickling wastes or concentrated plating solutions whether neutralized or not:

- Any waters or wastes containing iron, chromium, copper, zinc and similar objectionable or toxic substances; or wastes exerting an excessive chlorine requirement, to such degree that any such material received in the composite sewage at the sewage treatment works exceeds the limits established by the Inspector for such materials;

- Any waters or wastes containing phenols or other taste – or odor – producing substances, in such concentrations exceeding limits that may be established by the Inspector as necessary, after treatment of the composite sewage, to meet the requirements of the state, federal or other public agencies for such discharge to the receiving waters;

- Any radioactive wastes or isotopes of such half-life or concentration as may exceed limits established by the Inspector in compliance with applicable state or federal regulations.

- Any waters or wastes having pH in excess of 9.5 or less than 6.0;

- Materials which exert or cause:

- Unusual concentrations of inert suspended solids (such as, but not limited to, Fullers earth, lime slurries and lime residues) or of dissolved solids (such as, but not limited to, sodium chloride and sodium sulfate);

- Excessive discoloration (such as, but not limited to, dye wastes and vegetable tanning solutions);

- Unusual BOD, chemical oxygen demand, or chlorine requirements in such quantities as to constitute a significant load on the sewage treatment work; or

- Unusual volume of flow or concentration of wastes constituting “slugs” as defined herein; or

j.	Waters or wastes containing substances which are not amenable to treatment or reduction by the sewage treatment processes employed or are amenable to treatment only to such degree that the sewage treatment plant effluent cannot meet the requirements of other agencies having jurisdiction over discharge to the receiving waters.

3.	If any waters or wastes are discharged or are proposed to be discharged to the public sewers, which waters contain the substances or possess the characteristics enumerated in Section B.2 of this Article VI, and which in the judgment of the Inspector may have a deleterious effect upon the sewage works, processes, equipment or receiving waters or which otherwise create a hazard to life or constitute a public nuisance, the Inspector may:

- Reject the wastes;

- Require pretreatment to an acceptable condition for discharge to the public sewers;

- Require control over the quantities and rates of discharge; and/or

- Require payment to cover the added cost of handling and treating the wastes not covered by existing taxes or sewer charges under the provisions of Section G of this Article VI.

C.	Pre-Treatment and Flow Equalization.

1.	If the Inspector permits the pretreatment or equalization of waste flows, the design and installation of the plants and equipment shall be subject to the review and approval of the Inspector and subject to the requirements of all applicable codes, ordinances and laws.

2.	When preliminary treatment or flow-equalizing facilities are required by the Inspector, they shall be provided and maintained continuously in satisfactory and effective operation by the owner at his or her expense.

D.	Interceptors. Grease, oil and sand interceptors shall be provided by the owner and at the owner’s cost when, in the opinion of the Inspector, they are necessary for the proper handling of liquid wastes containing grease in excessive amounts, or any flammable wastes, sand, or other harmful ingredients, except that such interceptors shall not be required for private living quarters or dwelling units.  All interceptors shall be of a type and capacity approved by the Inspector and shall be located as to be readily and easily accessible for cleaning and inspection.

E.	Manhole Access. When required by the Inspector, the owner of any property serviced by a building sewer carrying industrial wastes shall install a suitable control manhole together with such necessary meters and other appurtenances in the building sewer to facilitate observation sampling and measurement of the wastes.  Such manhole, when required, shall be accessible and safely located and shall be constructed in accordance with plans approved by the Inspector.  The manhole shall be installed and maintained by the owner so as to be safe and accessible at all times and at the owner’s expense.

F.	Wastewater Testing. All measurements, tests, and analysis of the characteristics of waters and wastes to which reference is made in this resolution shall be determined in accordance with the latest edition of “Standard Methods for the Examination of Water and Wastewater, “published by the American Public Health Association, and shall be determined at the control manhole provided, or upon suitable samples taken at said control manhole.  In the event that no special manhole has been required, the control manhole shall be considered to be the nearest downstream manhole in the public sewer to the point at which the building sewer is connected. Sampling shall be carried out by customarily accepted methods to reflect the effect of constituents upon the sewage works and to determine the existence of hazards to life, limb and property.  (The particular analysis involved will determine whether a twenty-four (24) hour composite of all outfalls of a premise is appropriate or whether a grab sample or samples should be taken.)  Normally, but not always, BOD and suspended solids analyses are obtained from 24-hour composites of all outfalls whereas pH’s are determined from periodic grab samples.

G.	Special Agreements. Nothing in this resolution shall be construed as preventing any special agreement or arrangement between the District any industrial concern whereby an industrial waste of unusual strength or character may be accepted by the District for treatment, subject to payment therefor by the industrial concern.

Article VI: Liability of District:

A.	Duty of Care: The District will undertake to use reasonable care and diligence in order to prevent and avoid leaks, interruptions, and fluctuations in the service, but the cannot and does not guarantee that such will not occur.

B.	Limitation of Liability: Neither the District nor its agents or employees shall be liable for any inconvenience, loss, or damage done to any wastewater user, landowner, or any person claiming through any wastewater user or landowner, to any property of any such person, whether real or personal, caused by reason of: (i) any excess or deficiency in the pressure, volume, or supply of water due to any cause whatsoever, (ii) any break, leak or defect in, or by water or sewerage escaping from, service pipes or fixtures, whether owned or located on the property of the District or the user; or (ii) any interruption or disconnection of service authorized by these Rules and Regulations, regardless of whether notice of same was given.

Article VII:  Violations, Enforcement and Appeals.

A.	Violations. It shall be unlawful for any unauthorized person to:

1.	Maliciously, willfully, or negligently break, damage, destroy, uncover, deface or tamper with any structure, appurtenance or equipment which is a part of the Wastewater System;

2.	Connect roof downspouts, exterior foundation drains, areaway drains or other sources of surface runoff or groundwater to (a) a public sanitary sewer or (b) a building sewer or building drain which in turn is connected directly or indirectly to a public sanitary sewer;

3.	Place, deposit or permit to be placed or deposited in any unsanitary manner on public or private property within the District, or in any area under the jurisdiction of the District, any human or animal excrement, garbage or other objectionable waste;

4.	Discharge to any natural outlet within the District, or in any area under the District’s jurisdiction, any sewage or other polluted waters, except as permitted herein;

5.	Construct or maintain any privy, privy vault, septic tank, cesspool, or other facility intended or used for the disposal of sewage except as provided herein; or

6.	Otherwise violate any provision of this resolution.

B.	Enforcement. Depending on the nature of the provision at issue and the circumstances of the violation, a person violating any provision of this resolution may be subject to the following enforcement remedies:

1.	Immediate arrest and prosecution as allowed by the laws of Ste. Genevieve County;

2.	Service of a notice of violation by the District stating the nature of the violation and providing a reasonable time for the satisfactory correction thereof, within which time the offender shall permanently cease all violations;

3.	If a person continues a violation beyond the time provided for in the prescribed notice, such person upon conviction thereof shall be fined in an amount not exceeding $100.00 for each violation, and each day in which any such violation shall continue shall be deemed a separate punishable offense;

4.	Any person violating any of the provisions of this resolution may be subject to the suspension of water and sewer services by the District on reasonable notice thereof; and/or

5.	Any person violating any of the provisions of this resolution shall become liable to the District for any expense, loss, or damage incurred by reason of such violation.

C.	Appeals. Any aggrieved party may appeal the decision or action of: (1) the Inspector to the District for final determination, and (2) any decision or action of the District to the Cole County Circuit Court or other court or tribunal as may be allowed by law.

Section Two.

This Resolution shall be in full force and effect on and after its adoption and execution and as of December 31, 2020 or such earlier time as the District assumes ownership and control of the Lake Forest Estates Wastewater System.

ADOPTED by the Board of Trustees of the Lake Forest Estates Clean Water District, of Ste. Genevieve County, Missouri, this ______ day of ______________, 2020.

___________________________________

Duane Harley, Chairman

ATTEST:

______________________________

Don Kuehn, Secretary

(Seal)

CERTIFICATION

I, the undersigned, Secretary of the Board of Trustees of the Lake Forest Estates Clean Water District do hereby certify that the above and foregoing is a true and correct copy of Resolution #2020-009 establishing rules and regulations for the operation of the Wastewater System of the Lake Forest Estates Subdivision (as so acquired by the District and located in Ste. Genevieve County, Missouri) as the same appears of record in my office and as it was passed and approved by the Board of Trustees of the Lake Forest Estates Clean Water District. This resolution has not been altered, amended, or repealed as of this ____ day of ______________________, 20 ____.

________________________________

Don Kuehn

Secretary, Board of Trustees

Lake Forest Estates Clean Water District

Ste. Genevieve County, Missouri

(Seal)